## Slide 1: Model Blimp Design Competition Programming Workshop by Youth College (International) / VTC
---11 May 2019---

## Slide 2: Lecturer
Edmond Leung
Senior Lecturer
Youth College (International)
Vocational Training Council (VTC)
Email : whleung@vtc.edu.hk

## Slide 3: Wifi and file download
Wifi SSID:
YCI_2_4G / YCI_5G
Or
YCI_2_4G_2 / YCI_5G_2
Password:
ycinternational
PowerPoint and material download
//172.19.124.20
User : airship
Password : ycinternational

## Slide 4: Content
Background of Arduino and ESP8266 (D1 mini)
Installation of Arduino IDE and CH340 Driver for ESP8266
Arduino Programming Environment
Blink program on ESP8266
Basic C- Syntax : Variable, For loop, if… then… else…
Serial communication
Motor control on ESP8266 (analogWrite)
Android Wifi-hot and Wifi TCP/UDP Controller
Wifi (UDP package) between Android and ESP8266

## Slide 5: 1. Background of Arduino
The first Arduino was introduced in 2005.
A project for students at the Interaction Design Institute Ivrea in Ivrea, Italy
provide an inexpensive and easy way for hobbyists, students, and professionals to create devices that interact with their environment using sensors and actuators
Common examples for beginner hobbyists include simple robots, thermostats and motion detectors.

## Slide 6: Before Arduino
RS232
AVR Programmer
Development Platform
AVR Programmer
software

## Slide 7: Before Arduino
Improvement -> In System Programming

## Slide 8: Arduino IDE
Free development platform
USB programmable

## Slide 9: Arduino Boot loader
Simplified the programming process
Run User Program when startup
Detect New program from development platform
Arduino Boot Loader
User Program
Microcontroller Flash memory

## Slide 10: Arduino Board
An early Arduino board with an RS-232 serial interface (upper left)

## Slide 11: Arduino Board
An official Arduino Uno with descriptions of the I/O locations

## Slide 12: Arduino Board
Smallest Arduino Compatible Board

## Slide 13: Arduino Board
DIY Arduino Board

## Slide 14: Wifi + Processor => ESP8266
An integrated with Wifi microchip and microcontroller capability produced by manufacturer – Espressif Systems in Shanghai
IEEE 802.11 b/g/n Wifi (2.4G)
32-bit microcontroller
@ 80 MHz (default) or 160 MHz
32 KiB instruction, 80 KiB user data

## Slide 15: Pinout of D1 mini (ESP8266)
MiniUSB

## Slide 16: 2. Installation of Arduino IDE and CH340 Driver for ESP8266

## Slide 17: Step 1 : Arduino IDE and CH340 Driver for D1 mini (ESP8266)
Download and install the Arduino
https://www.arduino.cc/

## Slide 18: Step 2: USB-COM Driver
D1 Mini
(We are using)
USB
Using an IC (CH340) to convert signal between
RS232 (TTL signal) <-> USB

## Slide 19: Step 2: Install CH340 Driver
Download the CH340 Driver from the follow website
https://sparks.gogo.co.nz/ch340.html

## Slide 20: Step 2 : USB-COM Driver
For Official Arduino UNO
(Driver come with IDE)
For D1 mini through CH340 (We are using)

## Slide 21: Step 3 : install D1 mini on Arduino IDE
http://arduino.esp8266.com/stable/package_esp8266com_index.json

## Slide 22: Step 3 : install D1 mini on Arduino IDE

## Slide 23: Step 3 : install D1 mini on Arduino IDE
Search for ESP8266

## Slide 24: Step 3 : install D1 mini on Arduino IDE
INSTALLED Should be shown

## Slide 25: 3. Arduino Programming Environment

## Slide 26: Arduino IDE
Existing file name
IDE Version
Tools list
Program Code editing area
Message window
Arduino Board name and com port no.

## Slide 27: Arduino IDE - tools
Verify : Verify the program without error
Upload : upload program code after compile
New : open new file
Open : open existing file
Save : Save file
Serial Monitor : Communicate with Arduino through USB-serial port (Terminal)

## Slide 28: Arduino IDE – select board

## Slide 29: Arduino IDE – select COM port

## Slide 30: Upload LED Blink Example
Open example from
File
01. Basics
Blink

## Slide 31: 4. Blink program on ESP8266

## Slide 32: Upload LED (Arduino pin 2) Blink Example

## Slide 33: Arduino Programming
Setup() : a function run once at the start of a program that can initialize settings. In here LED_BUILTIN (2) used as output pin
Anything between /* and */
Will be ignored (For programmer give comments and remarks)
Anything after // will be ignored also
loop() : a function called repeatedly until the board powers off

## Slide 34: 5. Basic C- Syntax : Variable, For loop, if… then… else…

## Slide 35: C – Syntax – function
void setup( ) {
pinMode(LED_BUILTIN, OUTPUT);
}
void loop( ) {
digitalWrite(LED_BUILTIN, HIGH); // turn the LED off
delay(1000); // wait for a second
digitalWrite(LED_BUILTIN, LOW); // turn the LED on
delay(1000); // wait for a second
}
Function name
Output of the function (void mean nothing to output)
Input of the function () mean nothing input
Things to do of the function
Each instruction should be end with a ;
e.g. a = a + b;
All the instruction of the function should be with { and}

## Slide 36: LED Blink – Program Analysis 1
pinMode(LED_BUILTIN, OUPUT)
void setup( ) {
pinMode(LED_BUILTIN, OUTPUT); // define operation // mode of LED_Pin
}
void loop( ) {
digitalWrite(LED_BUILTIN, HIGH); // turn the LED off
delay(1000); // wait for a second
digitalWrite(LED_BUILTIN, LOW); // turn the LED on
delay(1000); // wait for a second
}
pinMode – function call to define pin mode
Function input 2 : operating mode
(INPUT, OUTPUT or INPUT_PULLUP)
function input 1 : target pin no.
(1 ~ 13 or A0 ~ A5)

## Slide 37: LED Blink – Program Analysis 2
digitalWrite(LED_BUILTIN, HIGH)
void setup( ) {
pinMode(LED_BUILTIN, OUTPUT); // define operation // mode of LED pin
}
void loop( ) {
digitalWrite(LED_BUILTIN, HIGH); // turn the LED
delay(1000); // wait for a second
digitalWrite(LED_BUILTIN, LOW); // turn the LED off
delay(1000); // wait for a second
}
digitalWrite – function call to set the target pin to output 3.3V or 0V
Function input 2 : Output status
(HIGH or LOW)
function input 1 : target pin no.
(D0 ~ D8 or A0)
delay – function call to introduce some delay in ms

## Slide 38: LED Blink – Program Analysis 3
void setup( ) {
pinMode(LED_BUILTIN, OUTPUT); // define operation // mode of LED pin
}
void loop( ) {
digitalWrite(LED_BUILTIN, HIGH); // turn the LED off
delay(1000); // wait for a second
digitalWrite(LED_BUILTIN, LOW); // turn the LED on
delay(1000); // wait for a second
}

## Slide 39: Using Variable to replace pin number
LED
2
“LED” is equal to 2
Declare a variable type as “byte” and name of the variable as “LED” and this variable is equal to 2

## Slide 40: Operation of variable
int abc = 18;
abc = 33;
abc
18
abc
33



## Slide 41: Operation of variable 2
int abc, def;
abc = 18;
def = abc + 10;
abc
18




abc
18
10
def

## Slide 42: Different type of variable
Type | Memory size | value
boolean | 8 bit (1 Byte) | 1 or 0
byte | 8 bit (1 Byte) | 0~255
char | 8 bit (1 Byte) | -128 ~ 127 (ASCII)
int | 16 bit (2 Byte) | -32768 ~ 32767
Long | 32 bit (4 Byte) | -2147483648 ~ 2147483647
float | 32 bit (4 Byte) | ±3.4028235 e+38
double | 32 bit (4 Byte) | ±3.4028235 e+38
char user = ‘L’;
int year = 2015;
float price = 199.99 ;
‘L’
2015
199.99

## Slide 43: PWM LED Luminosity control and analogWrite
By using the function – analogWrite
to Produce a PWM signal to dim the LED

## Slide 44: Concept of PWM
Pulse Width Modulation (PWM)
Using Pulses with different duty cycle to output a analog signal
* ESP8266 I/O pin output is 3.3V

## Slide 45: Concept of PWM
Parameter of PWM
Output voltage = Pulse Voltage x width / period

## Slide 46: PWM LED Luminosity control
analogWrite(LED, val)
int LED = 2; //define LED pin (PWM output)
// the setup function runs once when start-up
void setup() {
// initialize digital pin 3 as an output.
pinMode( LED , OUTPUT);
}
void loop() {
analogWrite(LED, 1023);
delay(100); // wait for 100 ms
analogWrite(LED, 768);
delay(100); // wait for 100 ms
analogWrite(LED, 512);
delay(100); // wait for 100 ms
analogWrite(LED, 256);
delay(100); // wait for 100 ms
analogWrite(LED, 0);
delay(100); // wait for 100 ms
}
analogWrite– function call to set the target pin to output 3.3V to 0V
Function input 2 : PWM pulse width
( 0 - 1023 )
0 = 0%, 1023= 100%
function input 1 : target pin no.
Repeat coding
How to improve it ?

## Slide 47: C – Syntax – For Loop
int a = 0;
for (int i=0; i<=10; i++)
{
a = a + 1;
}
For Loop Syntax
Initial value
Repeat condition
Increment method

## Slide 48: LED Dimming with for-loop
for (i=0; i<=1023; i++)
{
analogWrite(LED, i);
delay(1);
}
Initial value i = 2
Run the statement
when i less than or equal to 1023
Each time increase 1
Changing variable

## Slide 49: 6. Serial communication

## Slide 50: Concept of Serial communication

## Slide 51: Serial connection of D1 mini board
USB

## Slide 52: Serial Library

## Slide 53: Serial Communication
Serial.begin(115200);
Serial.print(“LED value :");
Serial.println(i);
Serial.begin– function call to setup a serial communication
function input 1 : communication speed
Print words inside “ and “
Print value

## Slide 54: Serial Communication
To open serial monitor

## Slide 55: Serial Communication
Send a char from PC to Ardunio to control LED Dimming
val = Serial.read();
Serial.read() – function call to check the serial port is there any character, if yes output to val
Serial.available();
Serial.available() – function call to check any serial data received, return 1 when there is data received

## Slide 56: Serial read and “if… else…” syntax
if( a == b )
{
// True instruction
}
else
{
// False instruction
}
Condition
e.g. a == b, a < b , a > b , a!=b

## Slide 58
Input area

## Slide 59: 7.Motor control on ESP8266

## Slide 60: Motor Drive  H bridge circuit
I/O pin of the microcontroller cannot provide sufficient current to drive the motor and may damage the I/O pin

## Slide 61: Motor Drive  H bridge circuit

## Slide 62: What is a motor Drive ?
DC MOTOR | Mode | IN1 | IN2 | IN3 | IN4
MOTOR-A | Forward | 1/PWM | 0 |  | 
 | Reversion | 0 | 1/PWM |  | 
 | Standby | 0 | 0 |  | 
 | Brake | 1 | 1 |  | 
MOTOR-B | Forward |  |  | 1/PWM | 0
 | Reversion |  |  | 0 | 1/PWM
 | Standby |  |  | 0 | 0
 | Brake |  |  | 1 | 1

## Slide 63: Serial control – PWM Motor Driver
Objective:
Read PC-Serial data to output different PWM pulses to drive motors
Hardware pin on D1 mini | Arduino Pin no. | Connected to Motor Drive Pin | Controlling Motor
D1 | 5 | Drive 1 – IN1 | Motor #1
D2 | 4 | Drive 1 – IN2 | 
D5 | 14 | Drive 2 – IN1 | Motor #2
D6 | 12 | Drive 2 – IN2 | 
D7 | 13 | Drive 2 – IN3 | Motor #3
D8 | 15 | Drive 2 – IN4 | 

## Slide 64
Read Serial from buffer
Check the serial date is equal to + or -
Update the motor PWM

## Slide 65: Serial control – PWM Motor Driver
Your turn :
Try to edit the program to control three motors

## Slide 66: 8.Android Wifi-hotspot and Wifi TCP/UDP Controller

## Slide 67: Share Wifi on Android Phone
1
2
3

## Slide 68: Share Wifi on Android Phone
4
5
6

## Slide 69: Share Wifi on Android Phone
Edit your own SSD and Password and note it down !
7
8
9
10

## Slide 70: Android Apps Setup
Download and install in Google Play
1
2
We will edit the IP later
8080
UDP
3
4
5

## Slide 71: Android Apps Setup (Visibility)
6
Enable the following button
Button2, Button4, Button5, Button6
Button8, Button11 & Button 19
7
8

## Slide 72: Android Apps Setup (Button Name)
9
10
Click on the button and edit their name
Button | Name
2 | Forward
4 | Left Turn
5 | Stop
6 | Right Turn
8 | Backward
11 | Up
19 | Down
11(After all 7 button is updated)

## Slide 73: Android Apps Setup (Command)
12
13
Click on the button and edit their name
Button | Command
2 | f
4 | l
5 | s
6 | r
8 | b
11 | u
19 | d
14 (After all 7 button is updated)

## Slide 74: Android Apps Setup (Display RX/TX)
16
17
18

## Slide 75: Android Apps

## Slide 76: 9.Wifi (UDP package) between Android and ESP8266

## Slide 77: Wifi(UDP) control – PWM Motor Driver
Objective:
Read UPD package from Wifi to control different PWM pulses to drive motors
PWM
PWM
Serial

## Slide 78: UDP connection testing using Example program

## Slide 79: UDP connection testing using Example program
Edit your own SSD and Password and note it down !
Update the SSID and Password same as your shared Wifi on Android
Change to 8080

## Slide 80: UDP connection testing using Example program
Upload
Open Serial Monitor

## Slide 81: UDP connection testing using Example program
The IP address of ESP8266 (D1 Mini)
The same IP also shown on your mobile phone

## Slide 82: UDP connection testing using Example program
Edit the IP address

## Slide 83: UDP connection testing using Example program
Button | Command
2 | f
4 | l
5 | s
6 | r
8 | b
11 | u
19 | d
When you click the Forward button, a ‘f’ command will send to ESP8266 through Wifi (UDP)

## Slide 84: Example program analysis 1
Using the Library of ESP8266WiFi & WiFiUdp
Data for Wifi connection
Variable to store the UDP content
Initialization of Wi-Fi Connection
Print out the Wi-Fi Connection details to Serial Monitor
Serial Monitor Initialization

## Slide 85: Example program analysis 2
Read the UDP packet and check anything received
Return package
Print out the Package details to Serial
Print out the Package content and print to Serial
We could insert program in here to control the motors by checking the content of “packetBuffet”

## Slide 86: Try to control the motors through your mobile phone
Adding
Define the variable to store motors speed
The initialization of I/O pins for motors
Checking the content of UDP and updating the I/O PWMs

## Slide 87: 1. Define the variable to store motors speed

## Slide 88: 2. The initialization of I/O pins for motors

## Slide 89: 3. Checking the content of UDP and updating the I/O PWMs

## Slide 90: Wifi(UDP) control – PWM Motor Driver
A reference program is provided
PWM
PWM
Serial

## Slide 91: CAUTION
Don’t change the motor direction Rapidly. This action may burnt the motor driver. ( You may develop a program to avoid this happen)
The motor provided is a 3.7V motor. Max output should be less then 500 in Arduino.
PWM
PWM
Serial
Directly
STOP
CW
CCW
CCW
CW

## Slide 92: Further development – close loop control
Height control
  Height sensor – MS5611
Direction control
  Inertial measurement unit - GY-LSM6DS3

## Slide 93: Q & A